Los Angeles Convention Center

Fire Department Requirements

The following are the Los Angeles City Fire Department's minimum requirements for shows and exhibits in the Los Angeles Convention Center.  No variance or alternate method of compliance shall be permitted from these requirements unless a written request is submitted and approved in writing by the Fire Marshal.

### Plans

Six copies of accurately scaled 1/32" = 1' floor plans of the show shall be submitted to the Fire Department at least 15 days before the opening date. Please note that booth location will be contingent on Fire Marshal approval of floorplans Submit plans as soon as possible to avert unanticipated delays and any relocation of booths.

Plans shall have Los Angeles Convention Center approval prior to submission to the Fire Department.  Plans shall show the size and locations of all aisle, exits, exhibits, decorator's booth, photographer's booth, registration booth, and other displays.  Show management is required to construct, operate, and maintain the show in accordance to the approved plan.

Department of Building and Safety Permit Requirements

All electrical equipment used or exhibited must be approved by Underwriter’s Laboratories or by the Department of Building and Safety Electrical Test Lab.

All natural gas appliances shall be of an approved type (i.e., A.G.A., U.L., or Gas Mechanical Lab), and shall be installed according to Los Angeles Building Department Plumbing Code.

Exhibits, booths, signs, partitions, and display counters, for temporary use, exceeding 12 feet in height or more than 24" above the floor (refer to page 2).

Outdoor tents or cloth structures for temporary use, not to exceed 120 days, and exceeding 450 square feet where they are accessory to permitted assembly use.

Fire Department Special Permits are Required in Order to:

- Display and operate any heater, barbecue, heat producing device, open flame device, candles, lamps, lanterns, torches, or other form of ignition.

- Display or operate any electrical, mechanical, or chemical device that is deemed hazardous by the Fire Department.

- Use or store flammable liquids, compressed gases, or other hazardous materials. When approved, the quantities shall not exceed 10 gallons used only for maintenance purposes and the operation of equipment when stored in approved containers and at approved locations. Storage in excess of 10 gallons that is used for maintenance purposes and operations of equipment shall be inside approved hazardous materials cabinets.  LIQUEFIED FLAMMABLE GAS is PROHIBITED inside any building.

- Display a motor vehicle or internal combustion engine.

- Operate any videotaping, television broadcasting, still photographic, or motion picture photographic equipment of commercial of professional purposes.

### Exits and Aisles

WHEN EXHIBIT HALL AREAS ARE USED IN DIFFERENT COMBINATIONS OR USED ALONE (HALLS AB; A; GHJK; GHJ; HJK; GH; JK)

- A clear cross aisle of at least 20 foot wide shall be maintained at approximately the center of the main floor running north and south or east and west.  EXCEPTION:  Hall "HJ" the 20 foot wide aisle must run east and west only.

- Other aisles, with the exception of the perimeter aisle, shall be a minimum of 10 feet.

- A clear, minimum 20-foot wide aisle shall be maintained the entire length of all exit doorways and shall be contiguous with all other required aisles.

- A clear space of at least 15 feet from in front of, and the width of, all operating concession stands shall be maintained.

- No variance or alternate method of compliance shall be permitted from these requirements unless a written request is submitted and approved in writing by the Fire Marshal.

### Additional Requirements

- Exit aisles and exit doorways, as designated on approved show plans, shall be kept clear and unobstructed.  Chairs, tables, easels, signs, etc. shall not extend beyond the booth area into exit aisles.

- No exit door shall be locked, bolted, or otherwise fastened or obstructed at any time an exhibit building is open for business.

- There shall be no obstruction blocking exit ways from the building to a public way, such as automobiles parked in front of doorways, barricades placed across sidewalks, or any similar obstruction.

- A clear access aisle of at least three feet shall be provided to all fire protection appliances, fire alarm boxes, and sprinkler valves.

- Exit ways shall not be obstructed by drapes or similar obstruction, unless such obstructions are on sliding rings and the color contrasts with the adjacent drapes, walls, or booths.

- Exit signs shall be clearly visible at all times.  Drapes, signs, or other similar obstruction shall not cover them.

### Booths

Covered booths having a cover at least 16 square feet, but NOT exceeding 750 square feet, shall be protected within by a smoke detector, which sounds a local alarm.

Covered booths within West Hall AB or South Hall G-K and Kentia Hall exceeding 750 square feet shall be protected within by a LAFD-approved automatic fire sprinkler system.  These systems must be installed under permit from the Department of Building and Safety and the Fire Department.  Sprinkler systems cannot be installed in any other areas of the building.

Vehicles/boats on display that are FOR SALE as part of the particular type of show may not require sprinkler systems.   Contact LAFD for permit and approval.

The total amount of covered area allowed in any separate space such as an exhibit hall, meeting room, or public space is 10% (1/10) of the total usable space.

Exhibitor booths are prohibited in corridors or lobbies.

Booths that exceed 750 square feet of space with enclosed perimeter walls, will require at least two separate exits and a construction permit from Building and Safety.  Additional exits may be required on a case-by-case basis (capacity will be computed at 15 square feet per person).

### Registration Pre-Function Areas

Six copies of accurately scaled 1/32" = 1' floor plans of the pre-function areas must be submitted to the Fire Department at least 15 days before the opening date or incorporated with the show floor plan showing construction and descriptive use of the areas.

Booth areas/exhibits are prohibited in all public areas except those authorized by LACC management and with Fire Department permit. Pre-function areas will be utilized for social interaction and pre-registration of attendees prior to attending or entering exhibits and meeting functions.  All required exit width through pre-function spaces will be maintained without obstruction.

### Combustible Decorations

All decorations, including, but not limited to drapes, table cloths that hang six (6) inches below the edge of the table, signs, banners, acoustical materials, cotton, hay, paper, straw, moss, split bamboo, wood chips, wood less than 1/4 inch (3/8 inch), foam core, etc., shall be flame retardant treated.  Glass or otherwise inherently fire retardant cloth may be used without being flame retardant treated.  Exhibitors shall present a California State Fire Marshal certificate of flame-retardant treatment or a sample of material for a field test upon request of the Fire Marshal.

Field flame test: A strip of material shall have a flame applied for approximately twelve (12) seconds.  The flame shall then be removed.  The material should self extinguish within two (2) seconds and/or not drip in flames.

Oilcloth, tar paper, sisal paper, nylon, orlon, and certain other plastic materials, cannot be made flame retardant.  Their use is prohibited.

### Combustibles

Literature on display shall be limited to reasonable quantities. Reserve supplies shall be kept in closed containers and stored in a neat and compact manner.

Rubbish, trash, and waste shall be removed from buildings daily.  Combustible waste materials, empty cardboard boxes, etc., shall be deposited in metal containers with metal lids until removed from the building.  Metal cans with tight fitting lids shall be provided for metal cuttings.  Cuttings shall be separated from ordinary combustibles.

### Projection Equipment

Projection equipment using electric arc or Xenon bulbs for illumination shall be installed under written permit from the Los Angeles Fire Department with the approval of the Department of Building and Safety.

### General Exhibit Hall Fire Regulations

- The show or exhibit will not be permitted to be open to the public, until all identified hazards have been alleviated.

- Special restrictions may be required to monitor and control hazardous conditions and operations not specifically covered by the above.

- Additional fire protection equipment may be required.  It shall be accessible, visible, and ready for immediate use.

- LACC is a non-smoking building.  Smoking is prohibited in all areas.

- The use of welding or cutting equipment for demonstration requires a written permit from the Fire Department.  The use of liquid flammable gas as a fuel source is prohibited.

- The demonstration or use of equipment using flammable liquid fuel in buildings is prohibited.

- Combustible liquids shall be used only under permit from the Fire Department.  They shall be stored or dispensed from an U.L. - approved safety can.

- All exits, hallways, and aisles leading from the building or tents are to be kept clear and unobstructed at all times.

- No exit door shall be locked, bolted, or otherwise fastened or blocked at any time an exhibit building is open for business.

- Liquefied flammable gases are prohibited inside buildings.

- Rubbish, trash, and waste shall be removed from buildings at the end of each working day. Metal cans shall be provided for metal cuttings, and cuttings shall be kept separate from ordinary combustibles.

- All electrical wiring shall be installed as per Los Angeles Building Dept. Electrical Code.

- Provide and maintain approved fire extinguishing equipment in all special areas as designated by the Fire Department.

- All sprinklers, standpipe hose cabinets, and fire alarm pull boxes shall be kept clear and unobstructed at all times.

- Cylinders of compressed gas, both combustible and non-combustible, shall be installed only by permit from the Fire Department, and shall be half-charged and firmly secured in an upright position.

- Exit signs shall be clearly visible.

- Flammable liquids shall be used only outside under permit from the Fire Department.  It shall be stored or dispensed from an U.L. - approved safety can with a maximum of one-day usage or one gallon, whichever is less, per booth.

- All appropriate local, state and federal guidelines shall be followed to appropriately dispose of all hazardous waste materials.

- Where combustible material cannot be removed from the area of operations, another person, competent in the use of fire extinguishing equipment, shall be assigned the duty of preventing or extinguishing any accidental fire that may occur during such operations.

For additional information, please call: Fire Prevention Bureau, Central Public Assembly

(213) 485-6050.